## Slide 1: http://observatory.microsoftspectrum.com
Created to provide an intuitive presentation of the usage of the wireless spectrum. The project is sponsored by Microsoft's Technology Policy Group and the data is made freely available to the public. Data is recorded through monitoring stations and is stored and processed for visualization through the Windows Azure cloud.

## Slide 2: Our Goals
<$5,000
Users
Large Scale
  Distributed to world-wide research orgs
Low Cost
  Suitable for large deployment
A global spectrum-monitoring platform:
Provides evidence (hard data) of the spectrum usage
Aids in policy and regulation decisions
Helps DSA systems

## Slide 3: Current Station Locations

## Slide 4: General Findings
Overall low total occupancy, time and location important, band specific

## Slide 5: Adding New Stations
Go to http://observatory.microsoftspectrum.com
Sign in to the site (registration is required to register a new station)
Click on the “Register New Station” button under where the sign in button was:
Hardware requirements, setup instructions, and links to monitoring software are displayed
Enter the information for the station (point of contact, location…)
Station will be approved by a Microsoft admin, and a station ID will be assigned

## Slide 6: Openness and Collaboration
Released under Apache 2.0 OSS license on CodePlex: https://spectrumobservatory.codeplex.com/
Working with university partners
  University of Washington
  MIT
  Rice
  UCSB
Full access to the all uploaded data available upon request. E-mail spectrum_obs@microsoft.com

## Slide 7: System Overview
Data
Control
Feature Vector Extraction
Smart Scheduling / Scanning
Custom Device Support
Local Process & Control
Cloud & Storage
Processed Data
Backwards
Control
USRP1(SBX)
400-4400MHz
USRP2(WBX)
50-2200MHz
Signal Splitter
Outdoor Antenna
Radio Frontend
Per USRP:
- Sampling Rate: 50 MS/s
- Instant BW: 40MHz
End User
Policy Makers
DSA Users
Researchers
• Real-time/History Occupancy
• User Signal Feature
• Other Information…
Visualize
Cmd

## Slide 8: Scanner
USRP1(SBX)
400-4400MHz
USRP2(WBX)
50-2200MHz
Signal Splitter
Outdoor Antenna
Radio Frontend
Per USRP:
- Sampling Rate: 50 MS/s
- Instant BW: 40MHz

## Slide 9: Scanner Configuration
Simple XML config file
<UsrpSequentialScanner cpuFormat = "fc64" fftAlgorithm = "n“ fullScale = "0“ minutesOfDataPerScanFile = "60" otwFormat = "sc16" peak = "0" rxRate = "25000000" samplesPerScan = "1024" multiThreadFft = "false" scanDirectory = "c:\spectrumdata\scan" secondsOfDataPerSample = "60" singleScan = "false" tuneSleep = "0" decibelShift = "0“ numberOfSampleBlocksToThrowAway = "0" numberOfSampleBlocksPerScan="1" scanOverlap="0" commChannel="serial" communicationsChannelLocks="false"
>
<Devices>
<add antenna = "RX2" clockSource = "internal" gain = "38" address="F49911" name="B200“ startFrequency= "70000000" stopFrequency= "5995000000" timeSource = "none" scanPattern = "StandardScan"/>
</Devices>
</UsrpSequentialScanner>

## Slide 10: Adding a New RF Sensor
Repeatable pattern to support various sensors
Step 1
    MS.Devices.USRP
    C# interop to sensor

## Slide 11: Adding a New RF Sensor (contd)
Step 2
    MS.Scanning.Scanners
    Configuration of sensor via XML config
    Implement algorithm specific to sensor for scanning

## Slide 12: Adding a New RF Sensor (contd)
Step 3
    MS.IO.ScanFile
    Output into standard file format

## Slide 13: System Overview
USRP1(SBX)
400-4400MHz
USRP2(WBX)
50-2200MHz
MIMO Cable
Signal Splitter
Outdoor Antenna
Radio Frontend
Per USRP:
- Sampling Rate: 50 MS/s
- Instant BW: 40MHz
Data
Control
Feature Vector Extraction
Smart Scheduling / Scanning
Custom Device Support
Local Process & Control

## Slide 14: New Feature Vectors (scanner side)
Single extensible file format (ScanFile)
Time
Config
Spectral Data
Moving to storing everything in this format for all raw data

## Slide 15: System Overview
Data
Control
Feature Matching
Smart Scheduling
Custom Device Support
Local Process & Control
USRP1(SBX)
400-4400MHz
USRP2(WBX)
50-2200MHz
MIMO Cable
Signal Splitter
Outdoor Antenna
Radio Frontend
Per USRP:
- Sampling Rate: 50 MS/s
- Instant BW: 40MHz
Cloud & Storage
Processed Data
Backwards
Control

## Slide 17: Metadata Storage
SQL Tables

## Slide 18: Raw Data Storage
Raw and Aggregated Azure blobs